Two persons are needed to safely assemble this product.

TOOLS- Screwdriver  (preferably electric screwdriver)

1   Lower one side panel on to base so that side supports rest on base and screw in at base line.

Repeat for other side panel.

Help will now be needed for a second person to hold sides upright and together.

2  Slide top-brace in to slots at the top of side panels (in centre).

Carefully place roof panel on top and screw in place.

3  Slide seat-base in on top of supports.

Push locating pegs in to holes (at the back) and pull back seat-base to rest against locating pegs.

Screw in place and remove locating pegs.

Push locating pegs into holes at seat level.

Slide seat-back in (in front of supports) and push up against locating pegs.

Screw in place and remove locating pegs.

4   Screw kick-board in to position on side panel supports and along bottom edge to base, using short screws.

Slide  monitor-shelf (lip upwards) and sliding-shelf unit in on runners at the required height for your system.  Fix securing bolt firmly in place at rear so as to prevent each shelf from moving back out of module.

See guidance notes

5    Slot seperator plate into position between supports on rear of seat-base.

Screw inspection panel to supports on side panels and bottom edge of seat-base.

(Speakers can be placed in this compartment before fixing this panel but it may be advisable to install all equipment after assembly is complete)

Back-panel with viewing-screen should be fitted with care.  Hold back-panel and slide top of viewing screen into slotted edge of roof-panel. Ease the back-panel down, bending the viewing screen, and push in to rest on inspection-panel. Screw in place using long screws.

Monitor-shield is fixed at the top edge to the roof-panel after your monitor has been installed.